## Slide 1: Information Technology concepts, components and Hands-on
MQTT

## Slide 2: The Information Technology
Mechanisms and technologies to handle the electronic data lifecycle
Software: a set of instructions and its associated documentations that tells a computer what to do or how to perform a task. Can be open-source or proprietary.
Application Software (e.g. word processors and browsers)
Operating Systems (e.g. Microsoft Windows and Ubuntu)
Development softwares (create Application and System software)
  Works with a programming language (e.g. C++)
Hardware: the physical parts that make up a computer or a device (e.g., processor, memory, and peripherals).
Are programmed by the vendor via firmwares, a software that provides low-level control or a simple operating environment
Two distinct hardware components are the Microcontrollers and Microprocessors
Windows XP is made of 45M lines of code
Notes: Mechanisms, such as storing, indexing, processing
Technologies, such as computers, networks and any other physical device
Lifecycle: creation -> (distributed) processing -> deletion
Type of softwares: https://simple.m.wikipedia.org/wiki/Software
Source Windows XP lines of code: https://www.facebook.com/windows/posts/155741344475532

## Slide 3: Arduino
A microcontroller-based board and a development software for the rapid prototyping
Inexpensive microcontroller platform
  Nano, Uno, Mega..
Cross-platform development software
  Arduino IDE
Open source and extensible software
  C++ libraries / AVR C
Open source and extensible hardware
  Breadboard version
  Functionalities via shields and (typically) breadboards
The Arduino Uno
The Arduino Ethernet shield
A breadboard
The Arduino IDE

## Slide 4: Arduino flavours
 | Boards |  | 
 | UNO (Rev.3) | Nano | Mega
Microcontroller | ATmega328P | ATmega328P | ATmega2560
Operating Voltage | 5V | 5V | 5V
Input Voltage (recommended) | 7-12V | 7-12V | 7-12V
Digital I/O Pins | 14 (of which 6 provide PWM output) | 22 (6 of which are PWM) | 54 (of which 15 provide PWM output)
Analog Input Pins | 6 | 8 | 16
DC Current per I/O Pin | 20 mA | 40 mA (I/O Pins) | 20 mA
DC Current for 3.3V Pin | 50 mA | / | 50 mA
Flash Memory | 32 KB (ATmega328P) of which 0.5 KB used by bootloader | 32 KB (ATmega328P) of which 2 KB used by bootloader | 256 KB of which 8 KB used by bootloader
SRAM | 2 KB (ATmega328P) | 2 KB (ATmega328P) | 8 KB
EEPROM | 1 KB (ATmega328P) | 1 KB (ATmega328P) | 4 KB
Clock Speed | 16 MHz | 16 MHz | 16 MHz
Length | 68.6 mm | 18 mm | 101.52 mm
Width | 53.4 mm | 45 mm | 53.3 mm
Weight | 25 g | 7 g | 37 g
Additional | Led at PIN 13, Reset button, ICSP | Led at PIN 13 | Led at PIN 13, Reset button, ICSP

## Slide 5: The Arduino IDE
Easy configuration
  Tools -> Serial Port
  Tools -> board
Connecting the board
  USB to power the board, upload the code and receive data
  Serial connection for debug (Serial Monitor) and communication
Arduino program
  Setup() and Loop()
  Program as C/C++
Notes: Follow https://www.tweaking4all.com/hardware/arduino/arduino-programming-course/arduino-programming-part-2/#YourBasicArduinoProgramLayout

## Slide 6: Assignment 1
15 minutes
Know your Arduino
Download and install the IDE
Connect the board and make on-board led blink

## Slide 7: The Grove prototypying system
A modular, standardized connector prototyping system
No jumpers or soldering
  Grove sensors plugged on the Grove shield
Documented sensors
  Libraries
  Expand the sketch provided for your development board (mainly Arduino and Raspberry Pi)
Verify version, type of sensor (Analog or Digital) and voltage

## Slide 8: Assignment 2
20 minutes
Connect the provided Grove sensor and follow the tutorial in the official documentation

## Slide 9: Assignment 3
20 minutes
Add one sensor and connect their features (e.g. turn on led if sensor signal the vibration)

## Slide 10: Raspberry Pi
Basically a small computer
Connectivity
  LAN, Wi-Fi and Bluetooth
Ports
  HDMI, audio, USB and LCD
Operating system
  Out-of-the-box usage
  Multi-tasking
Missing analog-to-digital converter
  But also supports Grove prototyping system

## Slide 11: Assignment 4
20 minutes
Install Arduino IDE on the Raspberry Pi and acquire sensor data using the emulated serial port